Ch.1 Questions:

- The truss element used in finite element analysis is considered as a two-force member element. List and describe the assumptions of a two-force member.

- What is the size of the stiffness matrix for a single element? What is the size of the overall global stiffness matrix in example 1.2?

- What is the first thing we should setup when building a new CAD model in Creo?

- How does the Creo Intent Manager assist us in sketching?

- How do we remove the dimensions created by the Intent Manager?

- How do we modify more than one dimension at a time?

- Identify and describe the following commands:

Ctrl	 +     Middle mouse button

Middle mouse button

Ch.2 Questions:

- Determine the coordinates of point A if the local coordinate system is rotated 15 degrees relative to the global coordinate system. The global coordinates of point A:  (30,50).

- Determine the global coordinates of point B if the local coordinate system is rotated 30 degrees relative to the global coordinate system. The local coordinates of point B:  (30,15).

Ch.3 Questions:

- List and describe two of the commands in MS Excel to perform matrix operations that were used in the tutorial.

- What is the difference between the ATAN2 function and the ATAN function in MS Excel.

- In MS Excel, the trigonometric functions require the associated angles to be in degrees or radians?

- How do we convert from an angle measurement from radians to degrees?

- What are the advantages of performing the direct stiffness matrix method to solve a 2D Truss problem using MS Excel versus using a calculator?

- Using MS Excel, determine the inverse matrix of matrix A:.

8         2       3      12      11

2         4       7     0.25     5

3         7       3       5        6

12       0.25    5       2        4

11         5       6       4        8

- Using MS Excel, determine the displacements of the following simultaneous equations:

25                8         2        3      12          X1

13.25           2         4        7     0.25       Y1

18                3         7        3       5          X2

19.25          12       0.25    5       2          Y2

Ch.4 Questions:

- Describe the typical finite element analysis steps.

- In the tutorial, how were the nodes and elements created in Creo Simulate?

- Can loads be applied to the midpoint of a truss element?

- How do you identify the ZERO-FORCE members in a truss structure?

- What are the basic assumptions, as defined in Statics, for truss members?

- What does BACS stand for?

- How is the X-axis of the BACS determined?

- What is the purpose of a beam release?

- How do we assign the material properties for truss element in Creo Simulate?

- How do we define the cross sections for truss elements in Creo Simulate? What standard cross sections are available in Creo Simulate?

- How do we determine the X and Y directions of an existing beam element in Creo Simulate?

- How do we determine the applied constraints on an existing system in Creo Simulate?

- How do we obtain the stress values of truss members in Creo Simulate?

- What is the type of FEA analysis performed in the tutorial?

# Ch.5 Questions:

- For a truss element in three-dimensional space, what is the number of degrees of freedom for the element?

- How does the number of degrees of freedom affect the size of the stiffness matrix?

- How do we create 3D points in Creo Simulate?

- In Creo Simulate, can we import a set of 3D point data that are stored in a regular text file?

- Will the Creo Simulate FEA software calculate the internal forces of the members?

- Describe the procedure in setting up the vector analysis of a 3D truss problem.

- Besides using the vector analysis procedure, can we solve the example problem by the 2D approach described in Chapter 4?

- Will Creo Simulate display the orientation of cross sections of truss elements correctly on the screen?

- Truss members are also known as two-force member, what does that mean?

- Can we use several different material properties to truss members in a truss system?

Ch. 6 Questions:

- For a beam element in three-dimensional space, what is the number of degrees of freedom it possesses?

- What are the assumptions for the beam element?

- What are the differences between Truss Element and Beam Element?

- What are the relationships between the shear diagram and the moment diagram?

- For beam elements, will the Creo Simulate FEA software calculate the reaction forces at the supports?

- Can we apply both a point load and a distributed load to the same beam element?

- How do we improve the quality of the curves shown in the shear and moment diagrams?

- For a 2D roller support in a beam system, how should we set the constraints in Creo Simulate?

- What are the main differences between a Creo Parametric Template file and a regular Creo Parametric part file?

- List and describe the general procedure to setup a display view in Creo Parametric .

Ch. 7 Questions:

- What are the main differences between the integrated mode and the independent mode of Creo Simulate?

- How do we account for inclined supports and apply angled loads on individual elements in Creo Simulate?

- Describe the method of Superposition.

- Can we create additional coordinate systems in Creo Simulate?

- Which command option do we use to display multiple result screens in the Review Results window?

- Will Creo Simulate calculate and display the reaction forces that are located at inclined supports?

- List the standard beam cross section types that are available in Creo Simulate.

- In Creo Simulate, list and describe the two options to establish beam elements you have learned so far.

- Are the Creo Simulate analysis results stored inside the Creo Parametric  part files?

- How do we control the speed of animation of the Creo Simulate analysis results?

Ch. 8 Questions:

- What are the equations of Statics (Equations of Equilibrium)?

- What is the type of structure where there are more supports than are necessary to maintain equilibrium?

- In the example problem, how did we solve the statically indeterminate structure?

- What is the quick key combination to dynamically Pan the 3D model in Creo Simulate?

- Is there any special procedure in setting up statically indeterminate structures in Creo Simulate?

- List and describe the differences between a CAD model and an FEA model.

- In Creo Simulate, what does Idealization mean?

- What are the differences in the way the FEA model was created in the tutorial vs. the approach done in the last chapter?

- Can the beam cross sections be changed after beam elements have been created?

- What is the percent error of the maximum bending stress obtained by the FEA analysis and the preliminary calculation in the tutorial?

Ch. 9 Questions:

- What are the four basic types of two-dimensional solid elements?

- What type of situation is more suitable to perform a Plane Stress analysis than a Plane Strain analysis?

- For plane stress analysis using two-dimensional elements, the surface of the mesh must be on which plane of a coordinate system?

- Which type of two-dimensional solid elements is most suitable for members that are thin and whose loads act only in the plane?

- Why is it important to recognize the symmetrical nature of design in performing FEA analysis?

- List and describe the advantages and disadvantages of the P-element method over the H-element method.

- Why is it important to not just concentrate on the stress results but also examine the displacements of FEA results?

- In the tutorial, did the change in the refinement of the P-elements helped the stress results? By how much?

- What does the Edge Distribution mesh option allows us to do?

Ch. 10 Questions:

- What are the most widely used failure criteria?

- What are the main objectives of finite element analysis?

- What will happen to the system if it is stressed beyond the elastic limit?

- What are the necessary elements to create a swept feature in Creo Parametric ?

- What is the purpose of doing a convergence study?

- Under what condition does the bending stress developed in a curved beam no longer linear?

- What does the Cutting/Capping Surfs option allows us to do?

- Can a curved beam problem be analyzed with the 1D beam element? What is the main limitation of performing such an analysis?

- What are the advantages of using 3D elements over using the 1D or 2D elements?

- What is the purpose of performing a multi-pass adaptive analysis?

Ch. 11 Questions:

- For designs that are thin and symmetrical about an axis, what are the different FEA analyses available in Creo Simulate?

- What are the advantages and disadvantages of performing an axisymmetric analysis over a 3D solid analysis?

- To perform an axisymmetric analysis in Creo Simulate, on which plane must the surface be created?

- In Creo Simulate, how do you setup the FEA model to be an axisymmetric model?

- To perform an axisymmetric analysis in Creo Simulate, which axis is the default axis of symmetry?

- To perform an axisymmetric analysis in Creo Simulate, can the surface be created in the negative X portion of the associated coordinate system?

- What are the requirements to apply constraints on thin shell models?

- How do you specify the thickness of a thin shell model?

- How do you display multiple analyses results on the same screen?

Ch. 12 Questions:

- What is the main purpose of performing a Modal analysis on a system?

- What are the relations between resonant frequencies and the natural frequencies of a system?

- In vibration analysis, any physical structure can be modeled as a combination of what objects?

- A cantilever beam can be modeled as a simple mass-spring system by examining the deflection at the tip of the beam, what is the equivalent spring constant for such a system?

- In performing a Modal analysis of a cantilever beam, would changing the material properties affect the natural frequencies of the system?

- In Creo Simulate, is it required to have a load applied to the system in order to perform a Modal analysis?

- In Creo Simulate, can we perform a Modal analysis without applying a constraint?

- For the cantilever beam with a mass attached at the end, when the attached mass is relative big, we can ignore the weight of the beam as a simplified approximation. Calculate the first natural frequency of the tutorial problem using this approximation and compare the results obtained.

# Text boxes

j

v

A

θ

u

50

θ

i

30

j

v

θ

B

u

30

15

θ

i

=